## Slide 1
Ανίχνευση Ακμών

## Slide 2: Τι θα δούμε σήμερα;
Ανίχνευση ακμών
  Τι είναι & που χρησιμεύει
  Ανίχνευση με κατωφλίωση και παραγώγιση
  Ανίχνευση με συνέλιξη
Συνήθεις τεχνικές
  Sobel edge detector
  Laplacian edge detector
  Canny edge detector
https://medium.com/@nikatsanka/comparing-edge-detection-methods-638a2919476e
depth discontinuity
surface color discontinuity
illumination discontinuity
surface normal discontinuity

## Slide 3: Η ιδέα
Ξεκινάμε με περιοχές όπου αλλάζει η κλίση

## Slide 5: Παράδειγμα: Ανίχνευση λωρίδας κυκλοφορίας
https://www.youtube.com/watch?v=Al4DnNkZUeA&feature=related&ab_channel=WeiLiu

## Slide 6: Είδη ακμών
step
ramp
roof
spike

## Slide 7: Σχέση σημείων σε εικόνα με εξαγωγή χαρακτηριστικών
flat
edge
‘line’
corner
‘dot’

## Slide 8: Πως υπολογίζουμε τις ακμές;
Use gradient G of intensity [I(x,y)] change, two methods
First order gradient
  I(x,y) is an edge if
Second order gradient (Laplacian operator)
  I(x,y) is an edge if
x
y
I(x,y)
I(x,y+1) I(x+1,y+1)
I(x,y) I(x+1,y)

## Slide 9: Με απλά λόγια
x
I(x,y)
x
x
1η παράγωγος: ελέγχουμε αν περνάει κάποια τιμή
2η παράγωγος: ελέγχουμε αν μηδενίζει
Ελέγχω την μεταβολή της φωτεινότητας κατά μια διεύθυνση

## Slide 10: Εναλλακτικός τρόπος: συνέλιξη
Εκτελούμε την πράξη της συνέλιξης μεταξύ μιας προκαθορισμένης μάσκας και της εικόνας
Exponential_and_Gaussian
Gaussian
Βοχ

## Slide 11: Ωπα! Πως πήγαμε από παράγωγο σε συνέλιξη;
Differentiate an image I w.r.t x. Denote as the gradient of
It is the same as:
(*) = Convolution operator
Gradient mask or filter mask

## Slide 12: Έχει κάποιο πλεονέκτημα;
Βασική υπόθεση: τα Gx,Gy είναι διαχωρίσιμα (separable). Τότε, το gradient Gm υπολογίζεται από τα:
Horizontal gradient, και vertical gradient,
An edge is found and direction is tan-1(Gy/Gx)=e
e

## Slide 13: 1-D convolution examples

## Slide 14: Sobel edge detection

## Slide 15: Image gradient
The gradient of an image:
The gradient points in the direction of most rapid change in intensity

## Slide 16: Από gradients στον Sobel
How would you implement this as a filter?
The gradient direction is given by:
The edge strength is given by the gradient magnitude
How does this relate to the direction of the edge?
-1 | 0 | 1
-2 | 0 | 2
-1 | 0 | 1
-1 | -2 | -1
0 | 0 | 0
1 | 2 | 1
Magnitude:
Orientation:

## Slide 17: Sobel operator
Original
Orientation
Magnitude

## Slide 18: Effects of noise
Consider a single row or column of the image
  Plotting intensity as a function of position gives a signal
Where is the edge?

## Slide 19: Effects of noise
Difference filters respond strongly to noise
  Image noise results in pixels that look very different from their neighbors
  Generally, the larger the noise the stronger the response
What can we do about it?

## Slide 20: Solution: smooth first
Where is the edge?
Look for peaks in

## Slide 21: Derivative theorem of convolution
Differentiation is convolution, and convolution is associative:
This saves us one operation:
f
Source: S. Seitz
How can we find (local) maxima of a function?

## Slide 22: Laplacian edge detection

## Slide 23: Υπενθύμιση: Derivative of Gaussian filter
x-direction
y-direction

## Slide 24: Laplacian of Gaussian
Consider
Laplacian of Gaussian
operator
Where is the edge?
Zero-crossings of bottom graph

## Slide 25: 2D edge detection filters
is the Laplacian operator:
Laplacian of Gaussian
Gaussian
derivative of Gaussian
Notes: How many 2nd derivative filters are there? There are four 2nd partial derivative filters.
In practice, it’s handy to define a single 2nd derivative filter—the Laplacian

## Slide 26: Edge detection by subtraction
original

## Slide 27: Edge detection by subtraction
smoothed (5x5 Gaussian)

## Slide 28: Edge detection by subtraction
smoothed – original
(scaled by 4, offset +128)
Why does
this work?

## Slide 29: Gaussian - image filter
Laplacian of Gaussian
Gaussian
delta function
Ωπ! Τι σου θυμίζει;

## Slide 30: Άλλο ένα παράδειγμα Λαπλασιανής
Top left: Original image.
Top right: After Gaussian blur filter.
Bottom Left: Apply Laplacian filter on the blurred image.
Bottom right: Edge after zero crossing

## Slide 31: Canny edge detection

## Slide 32: Canny Edge Detection
Optimal edge detector
Canny: "A Computational Approach to Edge Detection“
Criteria of optimality:
  low error rate, i.e., do not miss important edges and do not respond to non-edges
  edge localization, i.e., the distance between the edge pixels found and the actual edge is minimal
  one response, i.e., eliminate the possibility of multiple responses to an edge
https://towardsdatascience.com/canny-edge-detection-step-by-step-in-python-computer-vision-b49c3a2d8123

## Slide 33: Algorithm implementation: Step 1
Filter out any noise in the original image before trying to locate and detect any edges
Choose suitable Gaussian mask and convolve it with the image
The larger the width (σ) of the Gaussian mask, the lower the detector's sensitivity to noise
Example of Gaussian mask for σ = 1.4

## Slide 34: Algorithm implementation: Step 2
Find edge strengths by taking the gradient of the image
Use Sobel operators Gx and Gy
The magnitude, or edge strength, of the gradient is then approximated using the formula:

## Slide 35: Algorithm implementation: Step 3
Use gradient information in the x and y directions in order to find the edge orientation:
Caution, when Gx = 0:
  whenever Gy = 0, then there is no edge and θ will be arbitrary
  otherwise, when Gy  0, the edge orientation will be equal to 0 degrees

## Slide 36: Algorithm implementation: Step 4
Relate the edge direction to a direction that can be traced in an image.
Looking at pixel "a", the four possible directions are – 0o, 45o (positive diagonal), 90o and 135o (negative diagonal). Resolve edge orientation into closest direction.
X X X X X
X X X X X
X X a X X
X X X X X
X X X X X
5x5 subimage

## Slide 37
Algorithm implementation: Step 5
Apply non-maximum suppression (or how-to thin edges)
Nonmaximal suppression is used to trace along the edge in the edge direction and suppress any pixel value (sets it equal to 0) that is not considered to be an edge. This will give a thin line in the output image.
Picture from Prem K Kalra

## Slide 38
Algorithm implementation: Step 6
Eliminate streaking, i.e., the breaking up of the edge contour caused by the operator fluctuating above and below the threshold used to decide if a gradient strength should be considered an edge. (a.k.a. transforming weak pixels into strong ones)
Streaking can be eliminated by thresholding with hysteresis. Hysteresis uses 2 thresholds, a high T1 and a low T2. Any pixel in the image with a value greater than T1 is presumed to be an edge pixel, and is marked as such immediately. Then, any pixels connected to this edge pixel having a value greater than T2 are also selected as edge pixels.

## Slide 39
Canny Edge Detection (example 1/6)
Original image (left) — Blurred image with a Gaussian filter (sigma=1.4 and kernel size of 5x5)

## Slide 40
Canny Edge Detection (example 2/6)
Blurred image (left) — Gradient intensity (right)

## Slide 41
Canny Edge Detection (example 3/6)
Result of the non-max suppression.

## Slide 42
Canny Edge Detection (example 4/6)
Non-Max Suppression image (left) — Threshold result (right): weak pixels in gray and strong ones in white.

## Slide 43
Canny Edge Detection (example 5/6)
Results of hysteresis process

## Slide 44
Canny Edge Detection (example 6/6)
Original image on the left — Processed image on the right

## Slide 46: Τελεστής Κλίσης
η πρώτη παράγωγος μιας εικόνας υπολογίζεται ως το μέτρο της κλίσης
2
1
2
2
2
1
2
2
]
[
)
f
(
ú
ú
û
ù
ê
ê
ë
é
÷
÷
ø
ö
ç
ç
è
æ
¶
¶
+
÷
ø
ö
ç
è
æ
¶
¶
=
+
=
Ñ
| =
|Ñ
y
f
x
f
G
G
mag
f
y
x
y
x
G
G
f
+
| »
|Ñ
το μέτρο είναι μη γραμμικό
συνήθης προσέγγιση

## Slide 47: Μάσκα υπολογισμού κλίσης
z1 | z2 | z3
z4 | z5 | z6
z7 | z8 | z9
προσέγγιση με 2x2 μάσκες

## Slide 48: Άλλες 2x2 μάσκες
z1 | z2 | z3
z4 | z5 | z6
z7 | z8 | z9
Τελεστές Roberts

## Slide 49: Οι πιο δημοφιλείς μάσκες
z1 | z2 | z3
z4 | z5 | z6
z7 | z8 | z9
Τελεστές Sobel (3x3 μάσκες)
ο συντελεστής 2 χρησιμοποιείται για εξομάλυνση δίνοντας μεγαλύτερη σημασία στο κεντρικό pixel

## Slide 50: Σημείωση
Το άθροισμα των συντελεστών σε όλες τις μάσκες ισούται με το μηδέν ούτως ώστε η απόκριση των τελεστών σε περιοχές σταθερών αποχρώσεων γκρίζου να είναι μηδέν.

## Slide 51: Example of Combining Spatial Enhancement Methods
Enhancement steps:
Laplacian to highlight fine detail
Gradient to enhance prominent edges
Gray-level transformation to increase the dynamic range of gray levels
want to sharpen the original image and bring out more skeletal detail.
problems: narrow dynamic range of gray level and high noise content makes the image difficult to enhance

## Slide 53
Scale is selected through smoothing
Smoothing:
Eliminates spurious edges
Removes fine detail

## Slide 55
fine scale
high
threshold

## Slide 56
coarse
scale,
high
threshold

## Slide 57
coarse
scale
low
threshold

## Slide 58: Τέλος παρουσίασης!
Attneave's Cat (1954)